Instrumental Methods of Analysis

Spring 2008

If you feel that the questions are not understandable ASK.   It is never my intention to create exams that are beyond your capacity.

Partial credit is always given.  Each Problem is 10 points.

The take home part will be 10 points for each of two questions. The final grade will be normalized to 100 points.  The question will be posted on the web page by 8 pm tonight and is due in lecture on Tuesday next.

Look at the attached data, shown both in table and as a graph of signal vs time.   At some time after the beginning, t zero, the analyte was injected.

1)	What are the mean values and standard deviations associated with

A) the baseline (blank) and with

B) the signal?

2)	What is the LOD of the method?

What is the LOQ of the method?

3)	What is the resolution of the analyte from the baseline?

4)	What is the S/N for the data?

5)	Draw a circuit which will allow you to reduce the high frequency noise amplitude to 0.707 of its initial value   Derive the equation for this circuit.

6)	Estimate the rise time of the method.

7) 	Can you determine the concentration limit of detection?  If you can do so. Explain your answer.

8)	Explain what kind of instrumental changes in the data processing you could do to improve the S/N by a factor of 4?  Why would your strategy work?

10)	What is meant by GIGO?  Give one example that we have discussed the illustrates the concept of GIGO.

.